## Slide 1: Microelectronics, BSc course
Introduction
Szabó Péter Gábor, assoc. prof. (QB330)
szabop@eet.bme.hu
Poppe András, prof. (QB326)
poppe@eet.bme.hu
This presentation is available at: www.eet.bme.hu/~poppe/miel/en

## Slide 2: Microelectronics BSc. Course
Microelectronics usually means analog electronics design (mainly on chip level).
  Analog design in the BME ciriculum: Electronics 1.
  Microelectronics extends it with chip level considerations
  A.S. Sedra, K.C. Smith, Microelectronic Circuits, Oxford Series in Electrical and Computer Engineering 6th Edition, ISBN-13: 9780199339136
Related knowledge, skills
  Semiconductor and quantum physics, solid-state physics, semiconductor manufacturing technology, Mixed-signal CAD design, simulation methodologies, packaging, modern VLSI circuits, etc.

## Slide 3: Microelectronics BSc. Course
New skills and knowledge, modern technologies, methodologies:
  Operation, build-up, manufacturing of applied semiconductor devices (diode, transistor)
  Logic gates and standard cells
  Design methodology of modern ICs, VLSI circuits
  MEMS and optoelectronic devices, etc.

## Slide 4: Basics
We are interested in seeing the inside of these
Let’s have a look inside the package!
Integrated circuits (IC-s) on a surface mounted printed circuit board (PCB)
There are silicon chips inside

## Slide 5: Inside the package
Silicon die
Gold wire bonds
Lead frame, vias
Lid seal
Redistribution substrate

## Slide 6: Inside the package

## Slide 7: Basics
Wafer, die or chip:
  wafer made of perfect single Si crystal
There are many identical dies (chips) on a wafer
Wafer diameters: 15-20-25… cm or 4-6-8"
100…2000 dies/wafer, manufactured simultaneously

## Slide 8: Si single crystal wafers
DED, 2009
empty Si wafers:
2006
~1965

## Slide 9: Si single crystal wafers

## Slide 10: Crystalline structures
Solidification & Crystalline Imperfections Published by Blanche Parsons
Notes: https://slideplayer.com/slide/7070232/
Solidification & Crystalline Imperfections
Published byBlanche Parsons

## Slide 11: Results of crystallization
Mono-Crystalline Solar Cell
Poly-Crystalline Solar Cell
Notes: https://www.redarc.com.au/mono-vs-poly

## Slide 12: Manufacturing of single crystal wafers

## Slide 13: Si single crystal, wafers (2007: 12")
8" wafer with Pentium processors, Intel Museum
Finished Si wafer
~2007

## Slide 14: Manufacturing of wafers

## Slide 15: Basics
Finished wafers before dicing

## Slide 16: Basics
Dicing of a wafer
A finished wafer with dice (chips) on top
Diamond cutter

## Slide 17: Basics
A simple analog IC – microphotograph through an optical microscope
Features seem in different colors due to interference through SiO2 layers of different thickness:
A 741
Interference

## Slide 18: Basics
Intel Xeon 5600, 434 mm2
Notes: Egy subsztrát, hogy megbízható, gyors, párhuzamosítható, és közös erőforrást tudjon használni

## Slide 19: Basics
Intel Core i5-8400, 150 mm2
Notes: Egy subsztrát, hogy megbízható, gyors, párhuzamosítható, és közös erőforrást tudjon használni

## Slide 20: Basics
Intel Core i9-9900K, ~177 mm2 (unknown)
Notes: https://en.wikichip.org/wiki/i9-9900K

## Slide 21: Basics
Minimal feature size (MFS) – the smallest (thinnest) feature that you can create on the top of a silicon wafer (substrate)
SEM microphotograph
Metallization line ("wire")
Doped region ("diffusion line")
MFS in the early days: 15-20µm
MFS today: 10-14 nm or even less

## Slide 22: Basics
Minimal feature size (MFS) 2007/2008, Intel:
IBM
Many metallization layers, Cu instead of Al
Intel

## Slide 23: Basics
Minimal feature size (MFS) Intel 2012, 2014 (14nm)

## Slide 24: Basic processing principles
Layer growth or deposition: new material layer is formed over the entire surface of the wafer
Patterning: some patterns are formed in the deposited layer
  deposition of a photo-sensitive lack (photoresist)
  photographing the pattern onto the lack
  developing the photoresist: pattern formed in the resist layer
  transferring the pattern from the resist to the material layer underneath by some kind of etching
  removal of the resist
In-depth deposition of external material: ion implantation (formerly: diffusion)
Notes: Az egész Si tehcnológia lényege, hogy leválasztjuk, megmintázzuk és eltávolítjuk ami nem kell

## Slide 25: E.g. patterning
The original pattern is on a so called photo-mask
  made of chromium on glass substrate
  many times larger than a chip
Need for high level of accuracy:
  0.03µm over 30cm!
  10-7
Visible light:
  =0.3-0.6 µm
  deep UV needed!

## Slide 26: Making tiny structures (patterning)
Basic process: photolithography. Small features of a mask are photographed onto a lack called photo-resist
UV light is used
Resist is not sensitive to yellow
Our old facility
Our old facility
A fab somewhere in the world
Semiconductor Technology Lab, Microelectronics branch at DED

## Slide 27: Patterning: photolithography
Notes: SiO2 lesz az adalékolás maszkoló rétege
fotoreziszt felvtele
mintázat fényképezése a rezisztre
előhívás (oldás, hőkezelés)
mintázat átvitele a rezisztről az oxidre nedves marással

## Slide 28: Typical types of patterns on a chip
Metallization
Contact window
P diffused (doped) region
N diffused (doped) region
One process: 15..25 masks
Problem: alignment of masks
SEM of a resistor in an analog IC

## Slide 29: Basics
Layout: collection of all features on all material layers (and in-depth doped ones) which form the IC
Layout of a small IC as designed in the computer
Layout photograph of a small TTL IC (7400)
Circuit CORE
Bonding PADs
Notes: PAD a kommunikáció, külvilággal valló kapcsolat
Core: funkció megvalósítása

## Slide 30: Packaging: a great challenge today
Bonding machine
Many connections – fine pitch
high frequency properties
thermal properties

## Slide 31: Modern packaging – 3D integration

## Slide 32: Packaging – one of the big challenges
SoP - System on Package - Complete system integration
SiP - System in Package - is a number of integrated circuits enclosed in a single module (package)
SoC - System on Chip - integrates all components of a computer or other electronic system into a single chip.
LoC - is a device that integrates one or several laboratory functions

## Slide 33: The silicon fab
Cleanroom
Some process steps

## Slide 34: The cleanroom
Tiny structures are created on the surface of the wafers: high level of cleanness is required!
Special suit – like for astronauts
Special room: cleanroom; much cleaner than the operation room of a hospital

## Slide 35: The cleanroom
Intel Museum
IBM
EET cleanroom
Tiny structures are created on the surface of the wafers: high level of cleanness is required!

## Slide 36: The cleanroom
Notes: Fentről lefele, és olyan sebességgel, hogy ne legyen örvényes az áramlás

## Slide 37: The cleanroom

## Slide 38: Cleanroom at the DED
New semiconductor lab @ Building Q
Semiconductor Technology Laboratory,
Smart System Integration MSc minor spec.
Solar cells manufacturing

## Slide 39: Ion-implanter, diffusion furnace
IBM
DED, Building Q
Semiconductor Technology Lab, Microelectronics branch at DED
1200+ °C !!!

## Slide 40: A batch
Si wafers are processed in so called batches
40..100 wafers/batch, 10 000 – 50 000 chips/batch
Batch fabrication
Inserting a batch into a diffusion furnace

## Slide 41: Wafer sizes
Today at around 30cm in diameter (8") or even 12"

## Slide 42: An Intel fab

## Slide 43: Intel fab sites
Fab name | City | Production start year | Process (Wafer, node)
D1X | Hillsboro, Oregon, United States | 2013 | 300 mm, 14/10/7nm
D1D | Hillsboro, Oregon, USA | 2003 | 300 mm, 14/10/7nm
D1C | Hillsboro, Oregon, USA | 2001 | 300 mm, 22/14/10 nm
Fab 12 | Chandler, Arizona, USA | 1996 | 300 mm, 65 nm
Fab 32 | Chandler, Arizona, USA | 2007 | 300 mm, 14/10 nm
Fab 42 | Chandler, Arizona, USA | 2020[1] | 300 mm, 10/7 nm
Fab 11 | Rio Rancho, New Mexico, USA | 1993 (Closed) | 200 mm, 45/32 nm
Fab 11X | Rio Rancho, New Mexico, USA | 1995 upgrade 2020/2021 with 22/14 | 300 mm, 45/32 nm
Fab 17 | Hudson, Massachusetts, USA | 1998 (Closed) | 200 mm, 130 nm
Fab 24 | Leixlip, Ireland | 2006 | 300 mm, 14 nm
Fab 28 | Kiryat Gat, Israel | 2008 | 300 mm, 22/10 nm
Fab 68 | Dalian, Liaoning, China | 2010 | 300 mm, 65 nm 3DNAND, 3DXPoint[2]

## Slide 44: Intel fabs 2006-2008
65nm fabs, ~2006 45nm: "Fab32", 2007-

## Slide 45: History, trends

## Slide 46: Roots
1837 Morse, telegraph
~1920 radio reciever

## Slide 47: Microelectronics: fastest growing industry
Revolution of the transistors
Transistor – Bardeen (Bell Labs), 1947
Bipolar transistor – Schockley, 1949
The 1st bipolar logic gate – Harris, 1956
The 1st monolithic IC – Jack Kilby, 1959
The 1st commercial IC with logic gates – Fairchild, 1960
TTL – 1962..1990-ies
ECL – 1974..1980-ies
ECL 3-input Gate
Motorola 1966
You can make an IC of such a "complexity" in the cleanroom of the Department
Notes: Transistor–transistor logic (TTL) is a logic family built from bipolar junction transistors. Its name signifies that transistors perform both the logic function (the first "transistor") and the amplifying function (the second "transistor");
Emitter-coupled logic (ECL) is a high-speed integrated circuit bipolar transistor logic family. ECL uses an overdriven BJT differential amplifier with single-ended input and limited emitter current to avoid the saturated (fully on) region of operation and its slow turn-off behavior;
ECL RF-hez, kiszajú gyors

## Slide 48: Microelectronics: fastest growing industry
Development of the MOSFETs:
MOSFET transistor – Lilienfeld (Canada, 1925) and Heil (England, 1935)
CMOS – 1960s, stack due to manufacturing problems
pMOS processes in the 1960s
nMOS processes in the 1970s (4004, 8080)
CMOS processes from the 1980s – preferred MOSFET process due to low power consumption
Nowadays e.g.:
  BiCMOS, GaAs, SiGe – for very high frequency circuits
  SOI, Cu metallization, low-K dielectrics

## Slide 49: Gordon Moore, 1965:

## Slide 50: Microelectronics: fastest growing industry
Moore's law
In 1965 Gordon Moore predicted that in every 14..18 months the number of transistors integrated in a chip will double (exponential growth)
This prediction is valid even today.
The 1 million transistors/chip threshold was reached in the 1980s
  2300 transistors, 1 MHz clock frequency (Intel 4040) - 1971
  16 million transistors (UltraSPARC III)
  42 million transistors, 2 GHz clock frequency (Intel P4) - 2001
  140 million transistors, (HP PA-8500) – 1998
  ~3 billion transistors, (i7-9900K) - 2018
More than Moore: further increase of integration density, e.g. 3D stacking of chips (RAM-s, pen drives)

## Slide 51: Moore’s law
Result of 50 years of progress presented through a modern CPU and a processor of a modern smart phone

## Slide 52: Microelectronics: fastest growing industry
1971 -Intel 4040
2002 - Intel Pentium IV
2250 transistor
55 million transistor

## Slide 53: Microelectronics: fastest growing industry
2007 - Intel Core2 EE
2012 - Core i7
~600 million transistor
1 billion transistor

## Slide 54: Microelectronics: fastest growing industry
Notes: Embedded

## Slide 55: Prognosis: roadmap

## Slide 56: Recent – company webpages
Notes: Tick Tock

## Slide 57: Recent – company webpages
Notes: Tick Tock

## Slide 58
Minimal feature size – trend (Intel)
14 nm
2013

## Slide 59
Minimal feature size – trend (Intel)
Notes: Trigate

## Slide 60: Toplist of processors in 2015
Main features:
  clock frequency,
  CACHE size, organization
  Packaging
  die size,
  number of transistors
  power consumption

## Slide 61: A Moore's law for processors
Number of transistors doubles in almost every year

## Slide 62: Development of DRAMs
4-times growth in every 3 years
1.6-2.4 m
1.0-1.2 m
0.7-0.8 m
0.5-0.6 m
0.35-0.4 m
0.18-0.25 m
0.13 m
0.1 m
0.07 m
a page of A4 paper
an average book
2 h audio CD,
30 s HDTV
human brain,
human DNA

## Slide 63: Increase of the die size
2-fold growth in 10 years – 7% annual growth, corresponds to Moore's law
4004
8008
8080
8085
8086
286
386
486
Pentium ® proc
P6
1
10
100
1970
1980
1990
2000
2010
Year
Die size (mm)
Source: Intel

## Slide 64: Increase of the die size

## Slide 65: Clock frequency trend
2× every 2 years

## Slide 66: Power consumption trend
Continuous increase in case of processors
Limiting factor

## Slide 67: Increase in dissipation density
Power consumption growth faster than the die size
Cooling!!!
Dissipation density limits

## Slide 68: Cooling problem
Clock frequency stagnant

## Slide 69: More than Moore integration ITRS